## Slide 1: WiFi Based Indoor Positioning System
Under the guidance of “RIP NO GUDIENCE” YASH 170303105066 PREET 170303105067 AKHIL 170303105070
DEEP 170303105071

## Slide 2: Global Positioning System (GPS)
Prominent contributor in location tracking
Works efficiently in open areas
Used by many location tracking apps
Eg: Google Maps
Apple Maps OpenStreetMap

## Slide 3: Indoor Positioning
GPS needs an unobstructed line-of-sight to 4 or more satellites.
Fails inside enclosed spaces
Increasing need for Indoor Positioning inside Malls, Airports etc
No common existing system for Indoor Positioning
– Google’s experimental Indoor Map

## Slide 4: How can it be done ?
Radio Frequency Identification (RFID)
Bluetooth
WiFi
Motion Sensors & Position Sensors

## Slide 5: Why choose WiFi ?
Commonly available inside buildings
All smart phones come with inbuilt WiFi adapters
WiFi signal strength varies with distance
Can be used as a distance indicator for positioning

## Slide 6: Design Overview
Works in two phases.
  Calibration phase
  Positioning phase
Calibration phase
  Location Fingerprinting
Positioning phase
  Weighted K Nearest Neighbours Algorithm (WKNN)

## Slide 7: Location Fingerprinting
Received Signal Strength (RSS) values from multiple routers act as a fingerprint for a location
Different locations are most likely to have unique fingerprints
Fingerprint of ith location is denoted by ri
ri = {ri1, ri2, ri3,......,rim }
rij = RSS value of jth router from ith location

## Slide 8: Location Fingerprinting
Several locations are chosen and RSS values from them are recorded and form a radio map.
The recording at the ith location is of the form
(qi,ri)
qi - the geometric coordinates (xi,yi) ri - the location fingerprint

## Slide 9: Location Fingerprinting
A position estimator algorithm is used to find the coordinates of unknown location
9

## Slide 10: Weighted k Nearest Neighbour
The position estimator algorithm used is the Weighted k Nearest Neighbour (WkNN)
Finds the k nearest chosen locations from unknown location based on Euclidean distance
Calculates coordinates of unknown location as the weighted average of the nearest k points
10

## Slide 11: Weighted k Nearest Neighbour
Weight is the inverse of the Euclidean distance
k can be considered as a tuning parameter in the algorithm
When k=1, algorithm acts as a simple look up table
11

## Slide 12: How the algorithm works
12
1
2
3
4
Suppose there are 4 routers in the floor

## Slide 13: How the algorithm works
13
1
2
3
4
The signals emanating from routers leave a unique fingerprint at each location

## Slide 14: How the algorithm works
14
1
2
3
4
The signals emanating from routers leave a unique fingerprint at each location

## Slide 15: How the algorithm works
15
1
2
3
4
The signals emanating from routers leave a unique fingerprint at each location

## Slide 16: How the algorithm works
16
1
2
3
4
The signals emanating from routers leave a unique fingerprint at each location

## Slide 17: How the algorithm works
17
1
2
3
4
Choose 8 points on the floor and calibrate readings
(0,10)
(10,10)
(20,10)
(30,10)
(0,0)
(10,0)
(20,0)
(30,0)

## Slide 18: How the algorithm works
18
1
2
3
4
Calculate Euclidean distance from unknown point to all chosen points
Unknown Point

## Slide 19: How the algorithm works
1
2
3
4
Euclidean distance between points x and y is calculated by sqrt((rx1-ry1)2+(rx2-ry2)2+(rx3-ry3)2+(rx4-ry4)2)
19

## Slide 20: How the algorithm works
20
1
2
3
4
Nearest k points are chosen. Here k = 2.

## Slide 21: How the algorithm works
21
1
2
3
4
Coordinate of unknown location is the weighted average of the 2 nearest points
(10,10)
(10,0)
(10,4)
60
40

## Slide 22: Work Done
Prototype Android App created Performs calibration and positioning
Mapping done inside CSED Lab building
WkNN algorithm with k=1 used
Device position logs could be tracked from website

## Slide 23: Work Done
Application could distinguish the grids shown in the figure

## Slide 24
DEMO
AVAILABE SOON….
24
https://github.com/users/Preet-Dhorajiya/projects/1

## Slide 25: Practical Difficulties
Fluctuating signal readings
Considered the average of 30 readings
Readings might contain temporary APs
Prepared a list of trusted APs to be used
User orientation can affect the readings
Orientation specific readings should be recorded (to be done)
Proper positioning of APs can reduce error

## Slide 26: Work Remaining
WkNN should be modified to k>1 to increase accuracy
Ideal value of k needs to be figured
Readings taken should be normalised so as to work for all devices
Calibrated readings should be made available for all devices

## Slide 27: Questions?

## Slide 28: Thank You
28